## Slide 1: Indonesia NEP - Least cost electrification investment plan coordinated grid & off-grid access rollout, technology choice
Prepare a least-cost electrification roll-out plan for grid and off-grid communities to meet national targets by beneficiary type
Key digitized geo-referenced data layers for spatial least cost electrification rollout planning and costing platform
    - - Where are the MV lines today
  Population settlements and patterns
  Where are the schools, clinics, administrative centers
Earth Institute modeling platform – proof of concept funded and managed by World Bank (Kenya, Senegal, Rwanda)

## Slide 2
BEFORE: Electricity Access Maps Used Prior to EI Data Collection Efforts
(Eastern Indonesia, 9/2012)
Electrified Areas
Area Difficult to Reach
Medium Voltage
Constrained MV Plans due to Protected Forest
Diesel Plants
Notes: Blue dots: difficult to reach with grid electricity, either due to terrain or due to forestry protection.
2

## Slide 3: PLN staff training In Kupang, West Timor office for MV line data capture and digitization

## Slide 4: EI Team Supports Local Utility Workers to Create MV Grid Map with smartphones – hands on training by doing

## Slide 5
AFTER: MV Line Map Results from EI Data Collection Efforts
(Eastern Indonesia, 4/2013)
*Average line data collection rate by vehicle was
50-100km/day
(varies w/ road conditions)

## Slide 7
Satellite imagery or other high accuracy data source is used to geo-locate communities, including remote rural locations
Example Desa in Flores Island Group: Pondo, Lembor, NTT
Settlement Locations Data – nucleation patterns
1 km
Notes: 2 – Sub-Region area of SANO NGGOANG

## Slide 8
Communities are designated for grid expansion or off-grid systems based on least cost analysis
Example Desa in Flores Island Group: Pondo, Lembor, NTT
Coordinated grid and off-grid planning – target driven
1 km
Notes: 2 – Sub-Region area of SANO NGGOANG

## Slide 9: NEP - Grid-Rollout over next 20 Years Flores Island, Eastern Indonesia Maps Showing Optimal Mix of Grid vs Off-Grid Systems Least cost technology choices

## Slide 10
Notes: Scenario 231: @ 240 kWh per Year – Showing West Flores Proposed and Existing Grid

## Slide 15: All Flores Island Group

## Slide 16
West Flores Island

## Slide 17: Indonesia NEP Least cost electrification configurations by settlement size

## Slide 18
Grid “least-cost” expansion settlements
Chart: Bins: Number of Households per Settlement
| 0-10 | 11-20 | 21-50 | 51-100 | 101-250 | 251-500 | 501-1000 | >1000
Grid Connected | 0.21938 | 0.21132 | 0.18173 | 0.23177 | 0.357 | 0.67762 | 0.80223 | 0.91186
Proposed Grid | 0.23344 | 0.24484 | 0.38004 | 0.5239 | 0.5017 | 0.28485 | 0.19777 | 0.088143
Village Solar Mini-Grid | 0.038339 | 0.54384 | 0.43823 | 0.24433 | 0.1413 | 0.037528 | 0 | 0
Household Solar | 0.50884 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 19: Proposed Grid: 166,000 HHs Village Solar Mini-Grid: 84,000 HHs
Chart: Bins: Number of Households per Settlement
| 0-10 | 11-20 | 21-50 | 51-100 | 101-250 | 251-500 | 501-1000 | >1000
Grid Connected | 1030 | 3410 | 13086 | 20874 | 44311 | 37539 | 19256 | 22563
Proposed Grid | 1096 | 3951 | 27366 | 47185 | 62272 | 15780 | 4747 | 2181
Village Solar Mini-Grid | 180 | 8776 | 31556 | 22006 | 17539 | 2079 | 0 | 0
Household Solar | 2389 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 20: Grid connection in larger and densely nucleated settlements

## Slide 21
100m or 300 ft
Notes: On-site generation (source-agnostic), backup storage, metering.
Communications and information management systems.

## Slide 22
INSIDE SHED
STORAGE BATTERIES
METERING + COMM + uPROC
INVERTER+CC+BREAKERS
Notes: Shared solar idea in images – 90 seconds